## Slide 1: Network Security
Physical Network Security and Remote Access
Internet, Intranet, and Extranet Security
VPN and IPSEC
Firewalls

## Slide 2: Network Security at a Glance
Physical Networks (Layers 1-2)
(Ethernet, Token Ring, Wireless, ATM,
Frame Relay, X.25, FDDI, and many more)
Transmission Control Protocol (TCP)
Internet Protocol (IP)
Layers (3-4)
Applications
(Data, Voice, Video)
Physical
Network
Security
Internet
Security

## Slide 3
Physical Network Security -- LAN Security

## Slide 4: Remote Network Access Security
Remote access is popular with several people:
  Telecommuting employees
  Travelling employees
  Authorized partners and suppliers
  Customers who may need access to online order processing systems and order/trouble-ticket status.
  Network and system administrators who may need to diagnose and correct network and computer system problems without having to drive to work.

## Slide 5: Remote Access

## Slide 6: Internet Security
- Collection of TCP/IP Networks
- Public Internet, Intranet, Extranet

## Slide 7: NSPs and ISPs

## Slide 8: VPN for Internet Security
Virtual Private Networks (VPN)
  Data that is sent over public infrastructure needs to be secured
  Virtual private networks are private networks (e.g. networks internal to corporations) that use public communication infrastructure
  Encrypts the data before sending (symmetric key)
local network
Public network
local network
encrypted traffic
encrypted traffic
Non-encrypted traffic
Non-encrypted traffic

## Slide 9: Internet Security Protocol (IPSec)
Standard for VPN encryption (1992)
Provides security at the packet level (IP), instead of security at application layer - Part of IPv6
Encrypts and signs Headers and/or Data parts of IP Header
Security handled without requiring changes to applications
Issue:
  If the entire packet is encrypted, how will the routers know where to send info (destination address)
  destination headers are not encrypted or duplicated (encrypted, non-encrypted)
Can authenticate machines but not users -- too low level

## Slide 10
Corporate Intranet
(TCP/IP Network)
Firewall
Corporate Mainframe
Corporate LAN
Public
Internet
= Router
Mail Server
Remote
User
Branch
Office
= Remote Access
Server/Dialup Modem
Past Corporate Network Architecture

## Slide 11
Corporate Intranet
(TCP/IP Network)
Firewall
Corporate Mainframe
Corporate LAN
Public
Internet
= Router
Mail Server
Remote
User
Branch
Office
Current Corporate Network Architecture

## Slide 12: Corporate Network with VPN

## Slide 13
Extranet Security Example: ANX

## Slide 14: Firewalls Overview
Dual Home Firewall
- two network cards
- everything is checked
Router Firewall (Packet filtering)
- filtering addresses
- filtering traffic type (email)
Router
A) two networks are completely isolated
- Packets never transferred directly
- may be repackaged
- can run a proxy on the firewall machine
Net1
Net2
Net1
Net2
b) two networks are completely isolated
- Packets can transfer directly through router
- Some are sent to the firewall program e repackaged
- Firewall can run a proxy for repackaging, etc
Many commercially available firewalls: Altavista, Borderware (secure computing)

## Slide 15: Proxies as Firewalls
Web Server
Web
Browser
Web
Proxy
Web
Server
Non-Browser
Clients
Web
Browser
Proxies sit between clients and servers
Act as a server to client and vice versa
can be used for security, workload balance, etc

## Slide 16: Proxies as Firewalls
act on behalf of a server
can be a front-end to many clients
can handle security (used as a firewall) but can introduce security threat also (client not authorized but uses a proxy to fake authorization)
can translate requests (web to non-web)
can be used for caching
can provide anonimity to clients or servers
can be used for workload balance (more than one server)
can be used to filter requests and responses
Other uses?

## Slide 17: Packet Filtering Firewalls: IP (v4) Packet Format
Identifier
16
31
0
8
Version and Length
Type of Service
Length of datagram (bytes)
Flags and Fragment Offset
Fragmentation Control Fields
Time
Header Checksum
Source IP address
Destination IP address
Options and Padding
Data
Data

## Slide 18: TCP Port Number Examples

## Slide 19
Dimilitarized Zone
Web
App
Server
(include
Business
Logic)
HTML/XML
Documents
Firewall
Back-end
APPs and
Databases
Databases
Business
Internal Network
Security and
Directory Services
App
Server
Firewall
Customer
Site
Web- Internet (HTTP over TCP/IP)
External
Partners

## Slide 20: Firewall Policies and management
Filtering versus applications
  Filtering not strong enough for sensitive data (e.g., financial data)
  Proxies must be controlled carefully
  May need combination
To use a DMZ or not
  What should be in DMZ
Firewalls policies need to be established and monitored carefully
Firewalls only protect end-points
  what about transmission network

## Slide 21: Availability Versus Security Tradeoffs in Corporate Networks
Tradeoffs between security and availability must be considered while architecting a network security solution.
Redundant network equipment can increase system availability but it also can introduce security exposures.
For example, redundant routers, cables, and access points should be protected as diligently as the primary network equipments.
Fragmentation, redundancy, and scattering (FRS) techniques employed to increase the security as well as availability of software by fragmenting the messages and then routing them on multiple paths