## Slide 1: Wireless security
Issues in wireless security
Wireless Network Security
  Wireless LANs
  Cellular networks
  Satellite systems
  Other wireless networks: FSO, UWB, MANET
Wireless middleware and middleware security

## Slide 2: WIRELESS Security Issues
Information transmitted over wireless networks
  Wireless LANs
  Bluetooth and other personal area networks
  Cellular networks
  Satellite systems
  Fixed Wireless
  Other wireless networks: FSO, UWB, MANET
Main issue: information transmitted over common medium (air)
Security approaches at several levels (Networks to applications)

## Slide 3: Levels of Wireless Security
Applications
Middleware
Wireless
Link
802.11 security (WEP)
Cellular network security
Satellite link security
WLL and cordless link security
SSL and TLS
WAP security (WTLS)
Web security (HTTPS, PICS, HTTP Headers)
Proxy server security
SET for transaction security
S/MIME and PGP for secure email
Java security
Database security
TCP/IP
IPSEC and VPN

## Slide 4
Wireless Networks
Paging
Networks
Satellite
Systems
Cellular
Networks
Wireless LANs
Wireless
Local Loops
Example1:
GSM, 9.6 Kbps,
wide coverage
Example2:
3G, 2 Mbps,
wide coverage
Wireless
Ethernet
11 Mbps,
100 Meters
Example1:
FLEX, 1.2 Kbps
Example2:
ReFLEX, 6.4Kbps
Wireless WANs
Wireless MANs
Cellular
Networks
Personal
Area
Networks
Business
LANs
Bluetooth
1 Mbps,
10 meters
Example:
Motorola Iridium
up to 64 Mbps
globally
Example:
LMDS
10 Mbps,
100 Km
Wireless Networks at a Glance

## Slide 5: Wireless Ethernet LANs - 802.11
Wireless LAN Cell
Wireless LAN Cell
Wireless LAN Cell
Centrex
Router
Link to
Public Ethernet
T1
or
DSL
X
Y
Z
LAN Server
Wired Ethernet LAN
X, Y, Z are
access points
for the wireless
Ethernet LANs
A
B
C
D
A, B, C, D are
student laptops

## Slide 6: Vulnerability for 802.11Wireless LANs
Privacy Issues due to Random Connectivity. A user can potentially walk into a building and be connected to the access point by just being in the vicinity.
Identity Issues. In WLANs, the MAC address of the WLAN card is used as the only form of identity for both devices and users. Most current open source device drivers allow the users to change the MAC address.
Access Control Issues. Access control is usually based on ACLs (access control lists) that are based on identity (i.e., the MAC address). Since a MAC address can be changed, thus a malicious user can access someone else's ACL.
Authentication Issues. Several products use un-authenticated Diffie-Hellman (DH) algorithm for such an approach, But DH suffers from a well-known man in the middle attack as stated previously.
Availability issues due to possible jamming and denial of services attacks

## Slide 7: Approaches to Secure 802.11 LANs
  Use WEP as much as possible.
  WEP has several weaknesses but it is a good start
  Place the WLANs outside instead of inside the corporate firewalls. Force WLAN users to go through the firewall to access any corporate resources.
  Encrypt the wireless LAN traffic at higher level by using wireless VPN.
  Heavily protect the resources accessed through wireless LANs. For example, higher level security offered by SSL, PGP, and SET

## Slide 8: Wireless Personal Area Network (WPAN) Security
WPANs designed primarily for SOHO (Small Office Home Office) environments.
802.11 networks may be an overkill.
The main contenders for the WPAN are cordless phones, HomeRF and Bluetooth.
The emerging UWB (Ultra Wide Broadband) networks are a good contender mainly because of their strong security.
WPANs security issues are similar to the wireless LAN issues discussed previously.
Privacy, integrity, authentication, authorization, availability

## Slide 9: Bluetooth
Cellular
Network
PSTN
Access
Point
Wired
LAN
Bluetooth Piconet
(1 Mbps, 10 meters)
Mobile Adhoc
Networks (without
access point)

## Slide 10: A Cellular Network
Public
Switched
Telephone
Network
(PSTN)
Mobile
Telephone
Switching
Center
(MTSC)
Base Transceiver Station (BTS)
Mobile User
Cell 1
Cell 2
Cordless connection
Wired connection
HLR
VLR
HLR = Home Location Register
VLR = Visitor Location Register

## Slide 11: Security concerns unique to the cellular networks
The call setup information that includes the user ID and other information should be protected
The speech and data transmitted during a cellular conversation should be kept private and confidential.
Privacy of user location. The location (cell ID) from where the user is calling should be private and also the VLR/HLR records that trace where the user has been visiting should be kept private.
The calling patterns (e.g., calling home everyday at 5 PM to inform your family about when you will be home) should be private.
The user-ID in the cellular networks should be kept private.

## Slide 12: Security is improving with newer generations
1G
(<1Kbps)
1 Kbps
10 Kbps
100 Kbps
2 Mbps
1 Mbps
Data Rates
1980
1990
2000
2010
2G
(9.6Kbps)
2.5G
(10-150Kbps)
3G
(144Kbps to 2Mbps)
Years

## Slide 13: Satellite Security
US General Accounting Office (GAO) report found critical vulnerabilities in the nation's commercial satellite network.
Federal agencies using commercial satellites may be exposing sensitive data to unauthorized snooping.
The government uses encryption to protect satellite communications and employs physical security to protect ground stations
But many federal agencies rely on commercial satellite service providers
Commercial providers may not provide adequate security

## Slide 14: Satellite System Security
Encryption/
Spread Spectrum
Physical security
of earth station
Typically secured through scrambling of satellite by spread
spectrum techniques.
For additional security, the messages can be encrypted by using VPNs
Employing better physical security on ground stations.

## Slide 15: Wireless Local Loop Security
The security of WLL is addressed
by the IEEE 802.16 standard

## Slide 16: Emerging Wireless Network Security
Free-Space Optics (FSO)
Uses high intensity optical waves (lasers) to transmit information.
Used in wireless local loops
FSO transmission is among the most secure connectivity solutions (government and military use):
  FSO laser beams cannot be detected with spectrum analyzers or RF meters.
  FSO laser transmissions travel along a line of sight path that cannot be intercepted easily.
  An adversary needs to intercept a portion of the transmitted beam to intercept an FSO link, without exposing himself and his equipment.
FSO transceivers are typically installed high above street level. Interception efforts are quite difficult

## Slide 17: UWB
UWB provides high data rates (around 50 Mbps) in very short distances (10 meters).
UWB is a radio or wireless system that uses narrow pulses (on the order of 1 to 10 nanoseconds) for communication and sensing (short-range radar).
Originally developed for the military and classified for many years.
Very difficult to intercept

## Slide 18: Mobile ad hoc networks (MANETs)
Ad hoc networking is basically communication between stations without an access point.
Hosts rely on each other to keep the network connected.
Mobile host can communicate with other mobile hosts just by being in their vicinity.
Highly desirable in military situations (e.g., a battlefield) or emergency situations (e.g., a building that has been just demolished).
Principle challenge is vulnerability to security attacks.
Main problem: two mobile devices in a MANET can start communicating by just being in the vicinity of each other.
Active area of research and development

## Slide 19: Wireless Network Security Summary
It protects communications at the physical wireless link (layer 1 and 2) levels.
This type of security is especially important in wireless because of eavesdropping and other threats
It attempts to protect at least the segments of wireless links that need to be secured.
Need to develop some guidelines to deal with wireless security

## Slide 20: Some Guidelines for wireless Network security
  Turn on security at wireless links to avoid eavesdropping even if it is deficient.
  For example, use WEP because it does provide some security -- make up for WEP security by providing higher layers of security (e.g., SSL).
  Make sure that all access points are themselves monitored and controlled so that no one sets up rogue access points.
  Treat wireless networks as untrusted networks. Thus put the internal WLANs outside the firewall so that they are treated as outsiders.
  Minimize placing critical applications and databases on wireless networks;move them to wired networks behind firewalls.
  Make sure that the passwords on wireless networks are different than the wired networks. Hackers usually capture passwords from wireless networks and then use them to gain access over wired networks.

## Slide 21: Mobile IP Security
Mobile IP allow the system to recognize that you have moved
Send the results from your query to your new location
Main idea: same Internet connection address is maintained
Traffic is forwarded by using a "care of" address
Many security issues and evolving solutions

## Slide 22: WAP(Wireless Application Protocol)
Web Server
Content
CGI
Scripts
etc.
WML Decks
with WML-Script
WAP Gateway
WML Encoder
WMLScript
Compiler
Protocol Adapters
Client
WML
WML-Script
WTAI
Etc.
HTTP
WSP/WTP
Intended for data entry/display on cellular phones
“An open, global specification that empowers mobile users with wireless devices to
easily access and interact with information and services instantly.” www.wapforum.org
Complete protocol stack similar to Internet protocols but optimized for wireless
information pull and push transport layer and above; across multiple wireless technologies

## Slide 23: Figure 2: WAP Prototype
WAP
Devices
Web
Browser
WAP
Gateway
Web
Server
Servet
Content
(XML/HTML)
eCommerce
Module
HTML/XML
over HTTP
WML
over WAP
HTML/XML
over HTTP

## Slide 24: WAP Security Architecture
Web Server
CGI Scripts
WAP Gateway
Protocol Adapters
WML Encoder
WMLScript
Compiler
Wireless
network
with uses
WTLS
Security
WAP
Phone
Internet
uses
SSL
Security
Content
WML Browser
WML Script

## Slide 25: WAP Security
WAP specification ensures that a secure protocol is available for transactions on a wireless handset.
WAP uses Wireless Transport Layer Security (WTLS) protocol
  WTLS ensures data integrity, privacy, authentication and denial-of-service protection.
  WTLS does not support non-repudiation.
  Some WTLS messages can be sent without authentication of origin
WAP components can be attacked at several levels.
  WAP clients and servers
  WAP gateway
  WAP messages
Intrusion of WAP Gateway can have a very high impact on the WAP users.
It is important to secure the WAP Gateway through high levels of security. It should also be replicated.

## Slide 26: I-Mode
Very popular in Japan (around 20 Million users)
Competitor to WAP
Very heavy graphics oriented
WAP and I-mode may combine
NTT Docomo runs I-mode
Always on service (use GPRS)
9.6 Kbps at present - 3G later
Need a special I-mode phone, larger screens
I-mode sites have pre-fabricated content

## Slide 27: I-mode security
Financial
Institution
Web Server
with I-Mode
Content
Docomo
Wireless Network
using proprietary
protocols and
SSL
I-Mode
Phone
Dedicated
Lines
using SSL
Security

## Slide 28: Wireless Security Summary
Security concerns are more serious
Many areas of vulnerability
  Location services (HLR/VLR) are privacy concerns
  the current wireless access points present a large security problem.
  Mobile adhoc networks are concerns
  Several products use un-authenticated Diffie-Hellman (DH) algorithm which suffers from a well-known man in the middle attack.
  The Wired Equivalent Privacy (WEP) algorithm, part of the IEEE802.11standard for wireless LANs, is designed to protect wireless communication from eavesdropping.
  Several weaknesses of WEP have been demonstrated
Suggested approach:
  encrypt the wireless traffic
  heavily protect the resources accessed through wireless
  Provide higher level security or replace with stronger (e.g., FSO, UWB)